## Slide 1
Prologue: What is Petroleum Coke?
Petroleum coke is a carbonaceous solid-residual byproduct of the oil-refining coking process. Although petroleum coke is a relatively ‘dirty’ substance, this byproduct has potential given its high calorific content (28 MMBtu/ton LHV) and availability, more than 55 million tons in 2005 in the U.S.
Plot Summary
Petroleum coke is a major byproduct that historically has been used as a substitute for coal in power production or as a fuel in cement manufacture. The decreasing quality of crude oil refined in the United States means an increasing amount of petroleum coke is being produced, often with much higher metals and sulfur content.
Our objective is to evaluate a better route for using low quality petroleum coke by converting it into a high purity syngas for our linked acetic acid production team while capturing all of the sulfur, metals, and most of the CO2.
In our process, petroleum coke along with oxygen and steam are fed into an entrained flow gasifier to produce synthesis gas, a combination of carbon monoxide, hydrogen, carbon dioxide and hydrogen sulfide. Sulfur is a poison to downstream chemical production catalysts and must be removed from syngas to ppm levels.
Overall Reactions
Petcoke + O2 + H2O  CO + H2 + CO2 + H2S + Ash
Chapter 4: Syngas Preparation
Due to the relatively high amount of hydrogen sulfide and a ratio of CO to H2 that is not conducive to acetic acid synthesis, multiple sub processes are required to clean the syngas and adjust the CO to H2 ratio.
The Hydrogen Sulfide Removal and Claus Process are able to selectively remove H2S from the syngas and covert it to elemental sulfur.
The Water Gas Shift (WGS) allows the ratio of H2 to CO to be adjusted to 2.5.
Syngas Production From Petroleum Coke Gasification
From Low to High: A Story About Petroleum Coke and its Journey to Value
Authors: Russell Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Editors: Bill Keesom – Jacobs Consultancy; Jeffery Perl, PhD UIC Dept. of Chemical Engineering
Conclusion
With proper treatment petroleum coke can be converted from a low quality byproduct to a high quality syngas that can be used in chemical production to form a highly profitable product, in this case acetic acid. The Shell Gasifier, which is the backbone of the process, converts petcoke into a syngas. The biggest hurdle is the removal of sulfur and shifting the H2 and CO ratio, which is readily accomplished by the H2S absorption and WGS processes which are able to remove the impurities that label petcoke as ‘dirty’. In addition, capturing the CO2 from this process significantly reduces its carbon footprint.
Chapter 7: Economics
Chapter 1: Gasification
Gasification is the process of converting a carbon-rich feedstock into a highly usable synthesis gas. The term syngas means the gas is mainly composed of carbon monoxide and hydrogen but will contain impurities like HsS.
In our process the syngas produced must be cleaned, separated, and shifted to the proper ratio of carbon monoxide to hydrogen while utilizing the byproducts.
Ultimate Analysis
Component | Weight Percent
Carbon | 83.3
Hydrogen | 4.00
Nitrogen | 1.49
Sulfur | 6.14
Oxygen | 4.44
Entrained Flow Gasifier
(http://www.netl.doe.gov/technologies/coalpower/gasification/gasifipedia/4-gasifiers/4-1-2-3_shell.html)
Chapter 2: Process Overview
Chapter 5: Carbon Dioxide Capture
Carbon Dioxide is separated from the syngas through two absorption columns using Selexol as solvent. Carbon dioxide is then flashed off of the solvent and made capture ready. Capturing CO2 from this process reduces the greenhouse gas footprint to levels similar to that of bio feedstock based processes.
Chapter 6: Plant Layout
4923 Port Rd., Pasadena, TX
2.5 Miles West of Trinity Bay
Existing Roads and Railroads
140 Acres with Acetic Acid Production (Team Golf)
 | V | Ni | F | Cu | Mg | Se | Be | Pb | As | Cd | Hg
PPM | 325-2300 | 165-580 | 11 | 3.5 | 2.4 | <2 | 1.5 | .6 | .3 | .1 | <.01
Proximate Analysis
Component | Weight Percent
Fixed Carbon | 84.8
Moisture | 6.00
Volatile Matter | 8.60
Ash | 0.6
*Block flow diagram with stream data from our Aspen Plus steady state simulation
Average Metal Makeup
Chapter 3: Aspen Plus Simulation
Chart: Capital Cost Distribution ($321MM Total)
| Equipment Direct Cost | Land Cost | Engineering Cost | Plant Construction
 | 182 | 20 | 46 | 73
Total Equipment + Installation Cost | 
Process | Cost in MM$
Gasification Process | 135
H2S Removal | 14
Claus Process | 3
CO2 Capture | 26
WGS Reaction | 4
Total Direct Cost | 182
Economic Analysis | 
Capital Cost | $ 321 MM
Interest Rate on the Loan | 8.00 %
Inflation | 3.00 %
Syngas Price ($/ton) | $ 457.80
Sulfur Price ($/ton) | $ 70
NPV | $1,534 MM
IRR | 29.79 %
Payback Period | ~ 5.2 years
Overall Process Simulation
Notes: This template complements of MakeSigns.com
If you opened this file directly from a web browser, you’ll want to save it to your computer before adding your poster information.
This template has a page size of 36”x 48”. When uploaded at MakeSigns.com, this template can be used to order posters in the following sizes: 36”x 48”, 42”x 56”, 31.5”x 42”, and 27”x 36”.
We recommend that you avoid changing the page size of the template. Please keep in mind, if you do change the page size it will alter the available print sizes listed above.
Any changes to the template size should be done before entering your information.
If you have any questions about creating a scientific poster, visit MakeSigns.com or email us at support@graphicsland.com
©2009 Graphicsland