## Slide 1: syngas Production from petroleum coke gasification
Team Hotel:
Russel Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Advisors:
Bill Keesom – Jacobs Consultancy
Jeffery Perl, PhD – UIC Dept. Of Chemical Engineering
January 25, 2011

## Slide 2: Today’s Objectives
What we are doing?
  Gasification of petcoke to produce syngas
What do we have?
  Basics
    Feedstock and Gasifier
What can be expected in the future?
  Working calculations
  A better idea of scale
  Refined design basis

## Slide 3: What is Petroleum Coke?
A carbonaceous solid-residual byproduct of the oil-refining coking process
Reason for Selection
  Byproduct of heavy residue cracking
    Production steadily increased by 51% over decade(6)
  Inexpensive Cost ($15-20/ton)
  High Calorific content (~14,000 Btu/lb LHV) (1)
  Availability (Mainly Coastal)
    56.3 Million Tons in 2005 in U.S or 60% of world total(4)
Environmentally superior to coal and oil sand
Better manageability than MSW and Bio feed

## Slide 4: Types of Petroleum Coke
Different grades of Petcoke(1)
  Fuel grade: High in metals, sulfur, volatiles, moisture
  Anode grade: Low in metals, sulfur
    Moisture and volatiles removed (Calcined)
  Green vs. Calcined
  Variability due to feed grade of crude oil

## Slide 5: Competing Utilizations of Petcoke
66% of Petcoke is used as fuel grade coke
  Used in cement, paper and steel industry for heating
  Used a power generation source
34% is Calcined Petcoke
  Graphite anode for aluminum steel and titanium industry

## Slide 6: Composition of Petcoke(3)
Ultimate Analysis
Component | Weight Percent
Carbon | 83.3
Hydrogen | 4.00
Nitrogen | 1.49
Sulfur | 6.14
Oxygen | 4.44
Proximate Analysis
Component | Weight Percent
Fixed Carbon | 84.8
Moisture | 6.00
Volatile Matter | 8.60
Ash | .6
Element | V | Ni | F | Cu | Mg | Se | Be | Pb | As | Cd | Hg
PPM | 325-2300 | 165-580 | 11 | 3.5 | 2.4 | <2 | 1.5 | .6 | .3 | .1 | <.01
Average Petcoke Metal Makeup(5)

## Slide 7: Comparison: Coal vs. Petcoke(3)
Component | North Antelope Coal (wt%) | Petcoke (wt%)
Moisture | 26.6 | 6.00
Volatile Matter | 34.4 | 8.60
Fixed Carbon | 34.9 | 84.8
Ash | 4.14 | 0.60
Hydrogen | 6.85 | 4.00
Carbon | 51.8 | 83.3
Nitrogen | 0.64 | 1.49
Sulfur | 0.26 | 6.14
Oxygen | 36.3 | 4.44

## Slide 8: Design Basis
Commercial Scale Production
  Reaction Team Needs:
    1000-1100 tons per day of syngas
    CO:H2 ratio of 1:2
    Acetic Acid Production
  Our Side:
    We are looking large scale
    Typical petcoke gasification 2,000 tons/day(2)
    Estimate of necessary petcoke
Location
  The Gulf Coast

## Slide 9: Conceptual Proc Block Flow
Petcoke Storage
Pulverized or Slurred Feed
Gasifier
(Entrained Flow)
O2
Water
Slag
Syngas Cooling
Syngas
Heat Recovery Steam Generator
Steam
Steam Turbine
Power
Steam
Sulfur Removal / Recovery
CO2 Recovery
H2 & CO Separation
Syngas
Off to Chem. Production
Syngas Cleaning

## Slide 10: Gasifier Comparisons
 | Moving (Fixed) Bed | Fluid Bed | Entrained Bed
Outlet product gas temperature | Low (430-650°C) | Moderate (900-1040°C) | High (1230-1650°C)
Oxygen Demand | Low | Moderate | High (ASU required)
Steam Used | High | Moderate | Low
Internal Moving Parts | Yes | No | No
Product Gas | Hydrocarbons in gas | Lower carbon Conversion | High purity syngas, high carbon conversion
Feed Size | 6-50 mm | 6-10 mm | <0.1 mm
http://www.bqpes.com/gasification-tech-types.php
Notes: http://www.bqpes.com/gasification-tech-types.php

## Slide 11: Entrained Flow Comparisons
Type | Gasification |  |  |  |  | 
Gasification Technology | Texaco | E-gas | Shell | Prenflo |  | GSP
Feeding | Coal-water Slurry |  | Dry Coal |  |  | 
Particle Size/mm | <0.5 |  | <0.1 | <0.1 |  | <0.2
Gasification Temperature/°C | 1400-1600 |  | 1500-1900 |  |  | 
Gasification Pressure/Mpa | 1.0-6.5 |  | 1.0-3.0 |  |  | 
Slag Discharge Style | Liquid |  |  |  |  | 
Syngas Efficiency | 78 | 78-81 | >80 | >80 | 80 | 
Largest Production Scale(Single furnace) t/d | 2600 | 2500 | 2000 | 2600 | 720 | 
Reactor Wall | Refractory |  | Membrane |  | Cooling Jacket | 
http://www.starcontrols.com/Application/Application_min_e.asp?MinID=10
Notes: http://hotelgasifier2011.wikispaces.com/file/view/gasifier+selection.pdf

## Slide 12: Entrained Flow Gasifier
Large Capacity units
Gives minimal byproducts
Can supply the Syngas at higher pressures (1.0-6.5 MPa)
Short Residence time and high temperature operation (1400 – 1600 ⁰C)
High purity syngas and high conversion
Uses less steam
http://www.netl.doe.gov/technologies/coalpower/gasification/pubs/photo.html
Notes: http://www.bqpes.com/gasification-tech-types.php

## Slide 13: Syngas Comp. Vs. Temperature
http://maquettewicri.loria.fr/en.dcpr/index.php5?title=Image:DCPR_Biomass_Syngas_1.png
Notes: http://maquettewicri.loria.fr/en.dcpr/index.php5?title=Image:DCPR_Biomass_Syngas_1.png

## Slide 14: Potential Sources for Petcoke
Chevron
  Lemont, IL
Asbury Carbons
  Asbury, NJ
Oxbow
  West Palm Beach, FL

## Slide 15: Environmental Review
Air Pollution
Carbon Monoxide gas produced is highly toxic
Sulfur and Carbon Dioxide recovery allows for safe/environmentally friendly disposal
  Carbon Capture and Storage
Waste Water Concerns
Risk of Industrial Accidents

## Slide 16: Report Outline
Final Report:
  Executive Summary
  Discussion
  Recommendations
Appendices
  Design Basis: IP
  Block Flow Diagram: IP
  Process Flow Showing Major Equip.: N/A

## Slide 17: Report Outline
Appendices (Continued)
  Material and Energy Balances: N/A
  Calculations: N/A
  Annotated Equip. List: N/A
  Econ. Eval. Factored from Equip. Costs: N/A
  Utilities: IP
  Conceptual Control Scheme: N/A
  Major Equipment Layout: N/A

## Slide 18: Report Outline
Appendices (Continued)
  Distribution and End-use Issues: N/A
  Constraints Review: IP
  Applicable Standards: N/A
  Project Communications File: IP
  Information Sources and References: IP

## Slide 19: References
http://www.petcokeconsulting.com/primer/index.html
http://www.eia.doe.gov/oiaf/aeo/assumption/petroleum.html
http://www.osti.gov/bridge/
http://www.nationmaster.com/graph/ene_pet_cok_pro_fro_ref-energy-petroleum-coke-production-refineries
http://www.tappi.org/content/pdf/events/06energy-papers/6-3.pdf
http://www.anl.gov/PCS/acsfuel/preprint%20archive/Files/43_2_DALLAS_03-98_0257.pdf
http://www.powergenworldwide.com/index/display/articledisplay/125234/articles/power-engineering/volume-105/issue-10/news-update/study-predicts-lower-price-growing-demand-for-petcoke.html
http://www.epa.gov/hpv/pubs/summaries/ptrlcoke/c12563rr2.pdf

## Slide 20: References
http://www.netl.doe.gov/technologies/coalpower/gasification/gasifipedia/6-apps/6-2-6-2_Wabash.html
http://www.clean-energy.us/projects/eastman_power_magazine.htm
http://www.bqpes.com/gasification-tech-types.php
http://www.diversified-energy.com/index.cfm?s_webAction=hydromax
http://www.bqpes.com/gasification-tech-types.php
http://hotelgasifier2011.wikispaces.com/file/view/gasifier+selection.pdf
Eric Larsen and Ren Tingjin, "Synthetic Fuel by Indirect Coal Liquefaction," Energy for Sustainable Development 7 (2003) 79-80

## Slide 21: References
http://www.oxbow.com/
http://www.asbury.com/
http://www.chevron.com/
http://www.netl.doe.gov/technologies/coalpower/gasification/pubs/photo.html
http://www.starcontrols.com/Application/Application_min_e.asp?MinID=10