## Slide 1
Plot Summary
Petroleum coke is a major byproduct that historically has been used as a substitute for coal in power production or as a fuel in cement manufacture. The decreasing quality of crude oil refined in the United States means that more petroleum coke is being produced, often with much higher metals and sulfur content.
Our objective is to evaluate a better route for using low quality petroleum coke by converting it into a high purity syngas for our linked acetic acid production team while capturing all of the sulfur, metals, and most of the CO2 after combustion.
In our process, petroleum coke along with oxygen and steam are fed into an entrained flow gasifier to produce synthesis gas, a combination of carbon monoxide, hydrogen, carbon dioxide and hydrogen sulfide. Sulfur is a poison to downstream chemical production catalysts and must be removed from syngas to ppm levels by use of a physical solvent.
Syngas Production From Petroleum Coke Gasification
From Low to High: A Story About Petroleum Coke and its Journey to Value
Authors: Russell Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Editors: Bill Keesom – Jacobs Consultancy; Jeffery Perl, PhD UIC Dept. of Chemical Engineering
Prologue: What is Petroleum Coke?
Petroleum coke is a carbonaceous solid-residual byproduct of the oil-refining coking process. Although petroleum coke is a relatively ‘dirty’ substance, this byproduct has potential given its high calorific content (~14,000 Btu/lb LHV) and availability, more than 55 million tons in 2005 in the U.S.
Conclusion
With proper treatment petroleum coke can be converted from a low quality byproduct to a usable, high quality syngas and eventually be used in chemical production to form a profitable product, in this case acetic acid. The Shell Gasifier is the backbone of the process and turns petcoke into a usable syngas, all that was needed after wards is some fine tuning. The biggest hurdle was the removal of sulfur and shifting the H2 and CO2 ratio, but the Claus process and WGS is able to remove the impurities that labels petcoke as ‘low quality’.
Chapter 2: Project Overview
Block Flow Diagram showing stream totals (Tons/day)
Component | Weight Percent
Carbon | 83.3
Hydrogen | 4.00
Nitrogen | 1.49
Sulfur | 6.14
Oxygen | 4.44
Chapter 6: Cost Estimates
Chapter 1: Gasification
Entrained Flow Gasifier
Chapter 3: Syngas Preparation
Due to the relatively high amount of hydrogen sulfide and an improper ratio of CO to H2 in the produced syngas multiple sub processes are required.
The Claus Process / Sulfur Removal is able to convert the hydrogen sulfide in the acid gas to elemental sulfur and remove it from the syngas.
The Water Gas Shift (WGS) allows the ratio of H2 and CO2 to be adjusted to the required levels.
Chart: Equipment Cost
 | 135099254 | 17064712 | 30311530
NPV | $743,827,088 |  |  |  | 
IRR | 25.73 % |  |  |  | 
interest | 8% |  |  |  | 
Chart: Annual Operating Cost ($MM/YEAR)
| Raw Materials | Labor | CW+NG+Elec | Maintenance | Catalyst
($MM/YEAR) | 93.5 | 6.3 | 21.5 | 7 | 14.3
Chart: Cumulative Cash Flow ($MM/year) with $300/ton
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Cumulative Cash Flow ($MM/year) | -25.5466 | -129.5576 | -202.5478 | -177.4076 | -101.8074 | -24.1941 | 55.7011 | 137.945 | 207.7274 | 281.051 | 371.5388 | 465.0278 | 561.8017 | 661.9084 | 729.6319 | 837.0431 | 948.4421 | 1063.8781 | 1183.6821 | 1307.9077
Aspen Simulation (Hydrogen Sulfide Removal)
Chapter 4: Carbon Dioxide Capture
Petcoke Composition
Gasification is the process of converting a carbon-rich feedstock into a highly usable synthesis gas. The term syngas means the gas is mainly composed of carbon monoxide and hydrogen.
In our process the syngas produced must be cleaned, separated, and shifted to the proper ratio of carbon monoxide to hydrogen while utilizing the byproducts.
Carbon Dioxide is separated from the syngas through two absorption columns using Selexol as solvent. Carbon dioxide is then flashed off of the solvent and made capture ready. Utilizing this capture makes the overall process more appealing from an environmental view point.
Chapter 5: Plant Layout
4923 Port Rd., Pasadena, TX
2.5 Miles West of Trinity Bay
Existing Roads and Railroads
140 Acres with Acetic Acid Production (Team Golf)
Notes: This template complements of MakeSigns.com
If you opened this file directly from a web browser, you’ll want to save it to your computer before adding your poster information.
This template has a page size of 24”x 48”. When uploaded at MakeSigns.com, this template can be used to order posters in the following sizes: 24”x 48”, 36”x 72”, 42”x 84”, 18”x 36” and 21”x 42”.
We recommend that you avoid changing the page size of the template. Please keep in mind, if you do change the page size it will alter the available print sizes listed above.
Any changes to the template size should be done before entering your information.
If you have any questions about creating a scientific poster, visit MakeSigns.com or email us at support@graphicsland.com
©2009 Graphicsland