## Slide 1: Syngas Production from Petroleum Coke Gasification
Team Hotel:
Russel Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Advisors:
Bill Keesom – Jacobs Consultancy
Jeffery Perl, PhD – UIC Dept. Of Chemical Engineering
March 8, 2011

## Slide 2: Project Purpose
What we are doing
  Producing syngas from petcoke
  Using entrained flow gasifier
  Implementing a rigorous syngas cleaning
Why we are doing this
  Making syngas for acetic acid production
  Chemical production team specs
    CO to H2 molar ratio of 0.409
    CO2 and N2 mixed in
http://coalgasificationnews.com/tag/petcoke-gasification/
Notes: What we are doing, and why we are doing it
  2730 tons/day of syngas
  Desired CO to H2 ratio – 1:2.4 molar ratio
  Desired C to H ratio – 1:4.4 molar ratio
  Desired Temperature and Pressure
    400°F
    290 psia

## Slide 3: Review from Presentation 2
Discussed the Shell™ membrane gasifier
Discussed our syngas cleaning processes
  Sulfur Removal
  Claus Process
  Water Gas Shift
Flow Sheets
Early Material and Energy Balances

## Slide 4: Questions Brought Up Last Time
What was the heat rate brought up in the gasifier comparisons?
Why use N2 as a transport gas and not CO2?
How are we absorbing CO2?
What is a better definition of the quench?
Notes: Add fizz

## Slide 5: Agenda
Recent changes
  Using Selexol instead of MDEA
  Using the Superclaus
Aspen Simulation
Heat Load Identification
Economics
  Aspen Price Evaluator (ICARUS)
Equipment Sizing
Energy Balance
Location Update

## Slide 6: Flow Sheeting

## Slide 7: Flow Sheeting

## Slide 8: Flow Sheeting

## Slide 9: Flow Sheeting

## Slide 10: Flow Sheeting

## Slide 11: Flow Sheeting

## Slide 12: Heat Load Identification
Sulfur Cleanup
  Table showing stripper, flash , cooler & heat load
Claus Process
  Table showing furnace, flash, cat. reactor, cooler & heat load
Gasifier Section
  Table showing gasifier and syngas cooling

## Slide 13: Heat Sink Optimization
Stream Pre-heating
Lower Heater / Cooler Duties
Higher Duty vs. Heat Ex. Cost
Furnace
Cooler
HX
Acid Gas Cold
Acid Gas Hot
To Claus Catalysts
Hot Furnace Gas
Cold Furnace Gas

## Slide 14: Heat Loads
Gasifier Equipment | Heat Load (Btu/hr)
Gasifier | -34.7 x 106
HP Steam Heat Exchanger | 139.0 x 106
MP Steam Heat Exchanger | 281 x 106
COS Reactor | -4284
Cooler | -106.8 x 106
Flash | 2.99 x 106
Sulfur Clean Up Equipment | Heat Load (Btu/hr)
Sulfur Stripper Reboiler | 57.o x 106
Sulfur Stripper Cooler | -200.0 x 106
Selexol Cooler | -40.7 x 106
Rich / Lean Heat Exchanger | 274.9 x 106

## Slide 15: Heat Loads (Heat Duties)
Claus Process Equipment | Heat Load (Btu/hr)
Claus Furnace | -3.26 x 106
Condenser (Modeled Cooler and Flash) 1 | -31.3 x 106
Condenser 2 | -11.2 x106
Condenser 3 | -5.97 x 106
Condenser 4 | -3.92 x 106
Re-heater 1 | 9.72 x 106
Re-heater 2 | 5.29 x 106
Re-heater 3 | 3.46 x 106
Catalytic Reactor 1 | 3.03 x 106
Catalytic Reactor 2 | 1.72 x 106
Catalytic Reactor 3 | -5.73 x 106

## Slide 16: Energy Balance (Around WGS Reactor)
Inlet Fraction Clean Syngas Component Flow for WGS Reactor | (lbmoles/hr) for WGS | CP (btu/lbmole* F) | outlet syngas Comp (lbmole/hr) form (WGS)
CO | 4946.233 | 7.118 | 123.395
H2O | 6424.688 | 15.367 | 1601.850
N2 | 199.954 | 7.158 | 199.954
H2* | 2960.168 | 6.948 | 7783.006
CO2 | 469.211 | 10.559 | 5292.049
CH4* | 0.255 | 12.432 | 0.255
H2S | 0.000 | 0.000 | 0.000
COS | 0.000 | 0.000 | 0.000
Total | 15000.509 |  | 15000.509

## Slide 17
Gasification Process
$240,000,000
Solid Removal
Claus Process
CO2 Absorption
Water-gas Shift
Final syngas
product

## Slide 18
Gasification |  |  | 
 | SIZE | INDIRECT COST | DIRECT COST
Air Separation Unit | N/A | N/A | $100,000,000
Petroleum Coke Crusher |  | $ 5,401,890 | $ 7,022,455
Gasifier (2) | N/A | N/A | $ 132,000,000
Heat Exchanger |  | $305,740 | $ 642,060

## Slide 19
Solid Removal
$670,000
CO2 Absorption
Water-gas Shift
Final syngas
product
Sulfur Removal
Gasification Process
$240,000,000

## Slide 20: Solid Removal
 | SIZE | INDIRECT COST | DIRECT COST
Candle Filter |  | $ 364,770 | $ 510,680
Cyclone (remove fly ash) |  | $ 102,600 | $ 159,000

## Slide 21
Sulfur Removal
$9,300,000
Water-Gas Shift
CO2 Absorption
Final syngas
product
Solid Removal
$670,000
Gasification Process
$240,000,000

## Slide 22: Sulfur Removal
 | SIZE | EQUIP COST | TOTAL COST
Reactor (COS) |  |  | 
Reactor (CP) |  | $ 103,115.04 | $ 164,984.06
Absorber (CP) | 10737 cub. ft | N/A | $ 1,500,000.00
Absorber (CP) | 10737 cub. ft | N/A | $ 1,500,000.00
Stripper (CP) | 6636 cub. ft | $ 102,585.15 | $ 178,400.00
Stripper (CP) |  |  | 
Heat Exchanger (CP) | 1200 sq ft | $ 121,978.84 | $ 256,155.55
Cooler | 6739 sq ft | $ 168,800.00 | $ 320,600.00
Cooler | 440 sq ft | $ 16,700.00 | $ 79,200.00
Cooler | 258 sq ft | $ 13,600.00 | $ 73,600.00
Cooler | 163 sq ft | $ 11,800.00 | $ 69,800.00

## Slide 23
WGS Reactor
CO2 Absorption
Final syngas
product
Sulfur Removal
$9,300,000
$56,000,000
144 ft3
$360,000
Gasification Process
$240,000,000
Solid Removal
$670,000

## Slide 24: Co2 absorption
Equipment | Size | Cost | Direct Cost
CO2 absorber |  |  | 
CO2 Stripper | 2020 ft3 |  | 
Compressor |  | $272,889 | $ 409,333

## Slide 25
CO2 Absorption
$56,000,000
Final syngas
product
Solid Removal
$670,000
Gasification Process
$240,000,000
Sulfur Removal
$9,300,000
WGS Reactor
$360,000
$306,430,000

## Slide 26: Other Variable Cost
Type | Cost of year 1 ($/year) | Cost at the end of 25th year | Assumptions
Loan | $20.5 million | $ 1.5 million | Based on 6% interest
Cooling water | $1.9 million | $ 6.0 million | Based on 5% inflation rate
electrical | $1.8 million | $ 5.8 million | Estimated from a plant’s electrical cost
Salaries and fringes | $ 24 million | $ 77 million | average of 20 people/shift
Maintenance | $17 million | $ 55 million | 5 % of the capital cost
Royalties | $ 5 million | $15.8 million | 5% of production revenue
Insurance | $3.4 million | $ 11 million | 1% of the capital cost
Raw materials | $ 34 million | $107.6 million | 
Depreciation | $14 million | $14 million | Capital cost/25 years
Total | $121.6 million | $293. 1 million | 
Capital Cost as of now = $ 306,430,000
Estimated Revenue as of now = $ 94,000,000

## Slide 27: Other Fixed Cost
Other Fixed Cost
Maintenance
5% of Capital Cost
Laboratory Cost
30% Labor Cost
Insurance
License Fees and Royalties
2% of Capital Cost
1% Capital Cost
$ 4.7 million
$ 12 million
$ 5.4 million
$ 2.4 million
Capital Cost as of now= $ 306,430,000
Labor Cost as of now = $ 18,000,000

## Slide 28: Expected Revenue
Product and Side Products | Unit Price (per ton) | Unit Price (per year)
Syngas | $150.00 | $ 86.60 million
CO2 | $40.00 | $ 7.00 million
Sulfur | $10.00 | $ 0.30 million
Slag | TBD | TBD
Total | $200.00 | ~ $ 94 million

## Slide 29: Location
Victoria, Texas
Between Houston and Corpus Christi
200 acres
Kansas City Southern, Union Pacific, and Burlington Northern Santa Fe railways
Gulf Intracoastal Waterway

## Slide 30: Report Outline
Final Report:
  Executive Summary IP
  Discussion IP
  Recommendations IP
Appendices
  Design Basis: Done
  Block Flow Diagram: Done
  Process Flow Showing Major Equip.: IP

## Slide 31: Report Outline
Appendices (Continued)
  Material and Energy Balances: IP
  Calculations: IP
  Annotated Equip. List: IP
  Econ. Eval. Factored from Equip. Costs: IP
  Utilities: IP
  Conceptual Control Scheme: N/A
  Major Equipment Layout: IP

## Slide 32: Report Outline
Appendices (Continued)
  Distribution and End-use Issues: N/A
  Constraints Review: IP
  Applicable Standards: N/A
  Project Communications File: IP
  Information Sources and References: IP

## Slide 33: References
http://fossil.energy.gov/images/programs/sequestration/what_sequestration_lg.jpg
http://coalgasificationnews.com/tag/petcoke-gasification/

## Slide 34: CO2 Sequestration
CO2 in our syngas is absorbed on Selexol to be selectively removed
Delete only one CO2 slide.
Notes: One slide; Have what we are doing with CO2, What we are not doing (Shooting it into to the atm),
We are planning to transport the CO2 to the crude oil company, but we are still working on finding a better company. (Lipi)

## Slide 35
http://fossil.energy.gov/images/programs/sequestration/what_sequestration_lg.jpg