## Slide 1: Syngas Production from Petroleum Coke Gasification
Team Hotel:
Russell Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Advisors:
Bill Keesom – Jacobs Consultancy
Jeffery Perl, PhD – UIC Dept. Of Chemical Engineering
April 5, 2011

## Slide 2: Project Purpose
What we are doing?
  Producing syngas from petcoke
  Using entrained flow gasifier
  Implementing a rigorous syngas cleaning
Why we are doing this?
  Making syngas for acetic acid production
  Chemical production team specs
    CO to H2 molar ratio of 0.409
    CO2 and N2 mixed in
http://coalgasificationnews.com/tag/petcoke-gasification/
Notes: What we are doing, and why we are doing it
  2730 tons/day of syngas
  Desired CO to H2 ratio – 1:2.4 molar ratio
  Desired C to H ratio – 1:4.4 molar ratio
  Desired Temperature and Pressure
    400°F
    290 psia

## Slide 3: Overall Block Flow
Notes: VISIO, Update numbers, split streams to chem prod

## Slide 4: Recap
Discussed our Aspen Simulation
  Gasifier
  Sulfur Removal
  Water Gas Shift
  CO2 Removal
  Claus Process
Heat Loads
  Optimization
Equipment Costs and Sizes
Individual Economics
  Sensitivity Analysis
Location

## Slide 5: Agenda
PFD
Initial Control Scheme
Plant Layout (General Arrangement)
Calculations
Refined Economics

## Slide 6: PFD: Overall Process

## Slide 7: PFD: Gasification

## Slide 8: PFD: Hydrogen Sulfide Removal

## Slide 9: PFD: Claus Process

## Slide 10: PFD: Water Gas Shift

## Slide 11: PFD: CO2 Absorption

## Slide 12: PFD: CO2 Sequestration

## Slide 13: Control Scheme: H2S Removal

## Slide 16: Control Scheme: Water Gas Shift

## Slide 17: Plant Layout: Overall

## Slide 18: Plant Layout: Gasification Island

## Slide 19: Calculations

## Slide 20: Refined Economics: Raw Material Cost
Raw Materials | Quantity (lbm/day) | Price ($/lbm) | Total Cost (day) | Cost ($)/(year)
Petcoke (T/D) | 4,409,200 | 0.034 | $ 150,000 | $ 52,500,000
Zinc Oxide (lbm/day) | 392.73 | 55.00 | $21,600 | $ 7,560,053
Selexol | 6,200,000 | 3.20 | $19,840,000 | $ 19,840,000
Ferro-chrome | 53,001 | 1.33 | $ 70,492 | $ 24,672,215
Aluminium Oxide | 450 | 23.17 | $ 10,416 | $ 3,645,468
Oxygen | 4,232,832 | 0.028 | $ 117,120 | $ 40,992,000
Total |  |  |  | $ 149,209,735

## Slide 21
Chart: Annual Operating Cost
Chart: Annual Operating Cost
| Raw Material cost | Labor | CW+NG+Elec | Maintenance
($MM/YEAR) | 149 | 0.9 | 21.5 | 7

## Slide 22: Capital Cost Analysis
Chart: 
 | 135099254 | 17064712 | 30311530

## Slide 23: Economics Summary
 | 1st year | 2nd Year | 3Rd year | 4th year | 19th Year
Revenue | $ - | $ - | $ - | $ 129,570,000 | $ 240,352,994
Cap. Cost | $ 25,546,569 | $ 104,011,033 | $ 72,990,199 | $ 20,072,305 | $ -
Op. Cost | $ - | $ - | $ - | $ 111,070,226 | $ 242,943,820
Total Expense | $ 25,546,569 | $ 104,011,033 | $ 72,990,199 | $ 151,307,886 | $ 281,203,980
Income tax 40% | $ - | $ - | $ - | $ 13,144,845 | $ 83,909,549
Income After Tax | $ - | $ - | $ - | $ 19,717,268 | $125,864,323
Cumulative Cash Flow | $ 25,546,569 | $129,557,602 | $202,547,801 | $ 168,810,442 | $1,540,424,893
NPV | $89,282,710 |  |  |  | 
IRR | N/A |  |  |  | 
Interest | 8% |  |  |  | 

## Slide 24
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Cumulative Cash Flow ($MM/year) | -25.5466 | -129.5576 | -202.5478 | -168.8104 | -86.2094 | -0.66544 | 87.9245 | 179.6679 | 274.6769 | 358.8541 | 460.7492 | 566.2754 | 675.5651 | 788.7569 | 887.9895 | 1009.4259 | 1135.2183 | 1265.5321 | 1400.5405 | 1540.4249

## Slide 25: Sensitivity Analysis
Chart: NPV Vs. Syngas Prices
| 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 300 | 310
NPV | -45.3948 | 0.96237 | 47.3195 | 93.6767 | 140.0339 | 186.391 | 232.7482 | 279.1054 | 510.8912 | 557.2483

## Slide 26: Sensitivity Analysis
Chart: IRR vs. Syngas Price
| 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 300 | 310
IRR | -0.12391 | -0.02798 | 0.030288 | 0.073734 | 0.10922 | 0.13971 | 0.16677 | 0.19132 | 0.29172 | 0.30893

## Slide 27: Sensitivity Analysis
Chart: NPV Vs. Petcoke Prices
| 70 | 75 | 80 | 100 | 150
NPV | 528.7208 | 510.8912 | 493.0615 | 421.7428 | 243.446

## Slide 28: Sensitivity Analysis
Chart: IRR vs. Petcoke Price
| 70 | 75 | 80 | 100 | 150
IRR | 0.29843 | 0.29172 | 0.28491 | 0.25641 | 0.17264

## Slide 29: Conclusion
PFD
Control Schemes
Plant Layout
Calculations
Refined Economics

## Slide 30: Next Steps
Revise report

## Slide 31: Questions?

## Slide 32: References
Richard Parkinson. “Where Does It Go? An Introduction to the Placement of Process Equipment.” UOP PowerPoint. 2009. 2 April 2011.

## Slide 33: Report Outline
Final Report:
  Executive Summary IP
  Discussion IP
  Recommendations IP
Appendices
  Design Basis: Done
  Block Flow Diagram: Done
  Process Flow Showing Major Equip.: Done

## Slide 34: Report Outline
Appendices (Continued)
  Material and Energy Balances: Done
  Calculations: IP
  Annotated Equip. List: Done
  Econ. Eval. Factored from Equip. Costs: Done
  Utilities: IP
  Conceptual Control Scheme: Done
  Major Equipment Layout: Done

## Slide 35: Report Outline
Appendices (Continued)
  Distribution and End-use Issues: IP
  Constraints Review: IP
  Applicable Standards: IP
  Project Communications File: IP
  Information Sources and References: IP

## Slide 36: Control Scheme: CO2 Absorption

## Slide 37: Control Scheme: CO2 Sequestration

## Slide 38: Control Scheme: Gasifier

## Slide 39: Control Scheme: Claus Process

## Slide 40: Energy Balance Around WGS Reactor

## Slide 41: Energy Balance Around WGS Reactor
Inlet Fraction Clean Syngas Component Flow for WGS Reactor | (lbmoles/hr) for WGS | Cp (btu/lbmole* F) | Outlet Syngas Comp (lbmole/hr) from (WGS)
CO | 4946.233 | 7.118 | 123.395
H2O | 6424.688 | 15.367 | 1601.850
N2 | 199.954 | 7.158 | 199.954
H2* | 2960.168 | 6.948 | 7783.006
CO2 | 469.211 | 10.559 | 5292.049
CH4* | 0.255 | 12.432 | 0.255
H2S | 0.000 | 0.000 | 0.000
COS | 0.000 | 0.000 | 0.000
Total | 15000.509 |  | 15000.509

## Slide 42: Heat Loads
Gasifier Equipment | Heat Load (MMBtu/hr)
Gasifier | -34.7
HP Steam Heat Exchanger | 139.0
MP Steam Heat Exchanger | 281
Cooler | -106.8
Flash | 2.99
Sulfur Clean Up Equipment | Heat Load (MMBtu/hr)
Sulfur Stripper Reboiler | 57.0
Sulfur Stripper Cooler | -200.0
Selexol Cooler | -40.7
Rich / Lean Heat Exchanger | 274.9

## Slide 43: CO2 Sequestration
CO2 in our syngas is absorbed on Selexol to be selectively removed
Delete only one CO2 slide.
Notes: One slide; Have what we are doing with CO2, What we are not doing (Shooting it into to the atm),
We are planning to transport the CO2 to the crude oil company, but we are still working on finding a better company. (Lipi)

## Slide 44
http://fossil.energy.gov/images/programs/sequestration/what_sequestration_lg.jpg