## Slide 1: Syngas Production from Petroleum Coke Gasification
Team Hotel:
Russel Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Advisors:
Bill Keesom – Jacobs Consultancy
Jeffery Perl, PhD – UIC Dept. Of Chemical Engineering
March 8, 2011

## Slide 2: Project Purpose
What we are doing
  Producing syngas from petcoke
  Using entrained flow gasifier
  Implementing a rigorous syngas cleaning
Why we are doing this
  Making syngas for acetic acid production
  Chemical production team specs
    CO to H2 molar ratio of 0.409
    CO2 and N2 mixed in
http://coalgasificationnews.com/tag/petcoke-gasification/
Notes: What we are doing, and why we are doing it
  2730 tons/day of syngas
  Desired CO to H2 ratio – 1:2.4 molar ratio
  Desired C to H ratio – 1:4.4 molar ratio
  Desired Temperature and Pressure
    400°F
    290 psia

## Slide 3: Review from Presentation 2
Discussed the Shell™ membrane gasifier
Discussed our syngas cleaning processes
  Sulfur Removal
  Claus Process
  Water Gas Shift
Flow Sheets
Early Material and Energy Balances

## Slide 4: Questions Brought Up Last Time
What was the heat rate brought up in the gasifier comparisons?
Why use N2 as a transport gas and not CO2?
How are we absorbing CO2?
What is a better definition of the quench?
Notes: Add fizz

## Slide 5: Agenda
Recent changes
  Using Selexol instead of MDEA
  Using the Superclaus
Aspen Simulation
Heat Load Identification
Economics
  Aspen Price Evaluator
Equipment Sizing
Energy Balance
Location Update

## Slide 6: Flow Sheeting

## Slide 7: Flow Sheeting

## Slide 8: Flow Sheeting

## Slide 9: Flow Sheeting

## Slide 10: Flow Sheeting

## Slide 11: Flow Sheeting

## Slide 12: Heat Load Identification
Sulfur Cleanup
  Table showing stipper, flash , cooler & heat load
Claus Process
  Table showing furnce,flash,catreactor, cooler & heat load
Gasifier Section
  Table showing gasifer and syn cooling

## Slide 13: Heat Loads
Gasifier Equipment | Heat Load (Btu/hr)
Gasifier | -34.7 x 106
HP Steam Heat Exchanger | 139.0 x 106
MP Steam Heat Exchanger | 281 x 106
COS Reactor | -4284
Cooler | -106.8 x 106
Flash | 2.99 x 106
Sulfur Clean Up Equipment | Heat Load (Btu/hr)
Sulfur Stripper Reboiler | 57.o x 106
Sulfur Stripper Cooler | -200.0 x 106
Selexol Cooler | -40.7 x 106
Rich / Lean Heat Exchanger | 274.9 x 106

## Slide 14: Heat Loads (Heat Duties)
Claus Process Equipment | Heat Load (Btu/hr)
Claus Furnace | -3.26 x 106
Condenser (Modeled Cooler and Flash) 1 | -31.3 x 106
Condenser 2 | -11.2 x106
Condenser 3 | -5.97 x 106
Condenser 4 | -3.92 x 106
Re-heater 1 | 9.72 x 106
Re-heater 2 | 5.29 x 106
Re-heater 3 | 3.46 x 106
Catalytic Reactor 1 | 3.03 x 106
Catalytic Reactor 2 | 1.72 x 106
Catalytic Reactor 3 | -5.73 x 106

## Slide 15: Heat Sink Optimization
Stream Pre-heating
Lower Heater / Cooler Duties
Higher Duty vs. Heat Ex. Cost
Furnace
Cooler
HX
Acid Gas Cold
Acid Gas Hot
To Claus Catalysts
Hot Furnace Gas
Cold Furnace Gas

## Slide 16: Energy Balance
Energy Balance

## Slide 17: Economics
ECON

## Slide 18: Equipment Sizing
Equipment | Characteristic Size
Gasifier | 

## Slide 19: Location
Victoria, Texas
Between Houston and Corpus Christi
200 acres
Kansas City Southern, Union Pacific, and Burlington Northern Santa Fe railways
Gulf Intracoastal Waterway

## Slide 20: Report Outline
Final Report:
  Executive Summary IP
  Discussion IP
  Recommendations IP
Appendices
  Design Basis: Done
  Block Flow Diagram: Done
  Process Flow Showing Major Equip.: IP

## Slide 21: Report Outline
Appendices (Continued)
  Material and Energy Balances: IP
  Calculations: IP
  Annotated Equip. List: IP
  Econ. Eval. Factored from Equip. Costs: IP
  Utilities: IP
  Conceptual Control Scheme: N/A
  Major Equipment Layout: IP

## Slide 22: Report Outline
Appendices (Continued)
  Distribution and End-use Issues: N/A
  Constraints Review: IP
  Applicable Standards: N/A
  Project Communications File: IP
  Information Sources and References: IP

## Slide 23: References
http://fossil.energy.gov/images/programs/sequestration/what_sequestration_lg.jpg
http://coalgasificationnews.com/tag/petcoke-gasification/

## Slide 24: CO2 Sequestration
CO2 in our syngas is absorbed on Selexol to be selectively removed
Delete only one CO2 slide.
Notes: One slide; Have what we are doing with CO2, What we are not doing (Shooting it into to the atm),

## Slide 25
http://fossil.energy.gov/images/programs/sequestration/what_sequestration_lg.jpg