## Slide 1: syngas Production from petroleum coke gasification
Team Hotel:
Russel Cabral, Tomi Damo, Ryan Kosak, Vijeta Patel, Lipi Vahanwala
Advisors:
Bill Keesom – Jacobs Consultancy
Jeffery Perl, PhD – UIC Dept. Of Chemical Engineering
February 15, 2011

## Slide 2: Review from Presentation 1
Petroleum Coke Definition
Block Flow
Gasifier Comparisons
Environmental Concerns
  Location: Gulf Coast
  Sulfur Concerns
  CO2 Concerns

## Slide 3: Today’s Objectives
Discuss why we chose the Shell Membrane Gasifier
To present the overall process flow
  Gasifer
  Syngas Cleaning
    Sulfur Removal
  Water Gas Shift
To present our material and energy balance
Works in progress

## Slide 4: Project Purpose
Producing syngas from petcoke to be used by Team Golf for production of acetic acid
  2730 tons/day of syngas
  Desired CO to H2 ratio – 1:2.4 molar ratio
  Desired C to H ratio – 1:4.4 molar ratio
  Desired Temperature and Pressure
    250°F
    435 psi

## Slide 5: Process Overview
Gasifier
3086 tons/day of Petcoke
2997 tons/day of O2 / N2
708 tons/day of water
Syngas Cleaning/ Shift
6791 tons/day of Raw Syngas
2322 tons/day of CO
408 tons/day of H2

## Slide 6: Which Gasifier Fits Better with Our Needs?
Our Chem Production Team, Golf, requires pure syn gas with minimal amount of Sulfur.
We need more conversion of Sulfur to H2S, rather than to Carbonyl Sulfide because it is easier to remove H2S compare to Carbonyl Sulfide.

## Slide 7: SCGP better than E-Gas and Texaco
 | Shell |  | E-Gas |  |  | Texaco Q | 
Wall | Membrane Wall |  | Refractory Wall |  |  |  | 
Feedstock | Dry |  | Slurry |  |  |  | 
Syngas Conversion | Higher than 99% |  | Lower than 99% |  |  |  | 
 | Lower |  | Higher |  |  |  | 
 | 8,370 | 10,350 | 8,550 | 11,000 | 9,300 |  | 11,300
Quench | Quenching by recycle |  | Chemical Quench (forms tar) |  | Radiant Syngas cooler (Forced five Outages) |  | 
Notes: http://www.andrew.cmu.edu/user/kmeister/egroup/bin/Holt_SummaryIGCC_Cost_CCS_03.pdf

## Slide 10: Quench
At the outlet of the gasifier reactor the temperature of the syngas is around 1500°C and the fly ash (or slag) is in liquid form. To protect downstream process equipment from fouling, a quench is needed to solidify the slag and make it non-sticky.
There are four types of quenches:
  Water quench
  Radiant quench
  Quenching by Recycle
  Chemical quench

## Slide 11: Quenching By Recycle
Used in Shell Coal Gasifier
After particle removal in the candle filter, about half of the syngas flow which has a temperature around 600°F is recompressed and recycled to the gasifier outlet.
By mixing the 2700°F hot syngas with the recycle stream, a cooling down to around 1650°F is achieved.
Heat is then recovered in a convective syngas cooler.

## Slide 12: Syngas Cleaning
Raw syngas sent to DSR then through a filter
Raw syngas is sent to an absorber
  MDEA (methyldiethanolamine)
  Solvent Regeneration (Reboiler)
Second absorber section for CO2 removal
H2, CO, and very litte CO2 sent to WGS
H2S in acid gas sent to Claus Plant

## Slide 13: Claus Plant
H2S burnt in a furnace with O2 and air
  H2S + 1½ O2 ←→ SO2 +H2O
  2 H2S +SO2 ←→ 2 H2O+ 3/8 S8
  3 H2S + 1½ O2 ←→ 3 H2O+ 3/8 S8
Heated, passed over an alumina catalyst, and condesned multiple times
  Combusted at 1832 - 2192°F
  Cooled then reheated to 392 - 572°F for reactors
  3 Claus reactors

## Slide 14: WGS Blocks
An reversible exothermic reaction
  CO + H2O < ---- > CO2 + H2 ( -17,706 BTU/lb-mole)
Equilibrium dependant on temperature but not pressure
Typical shift are done in two steps a hot and a cold
Catalysts
  Ferro-Chrome (Fe3O4 Cr2O3) for HTS
  Copper Zinc (Cu Zn) for LTS
    Cobalt Molybdenum (Co Mb) for sulfur contents LTS
HTS
750 F
Cooler
LTS
390F

## Slide 15: Flow Sheets

## Slide 16: Flow Sheets (Part 1)

## Slide 17: Flow Sheets (Part 2)

## Slide 18: Material Balance Assumptions
Assuming petcoke is converted according to literature
Assuming only 90% (mole) CO2 is absorbed into absorbers along with all H2S, COS, H2O
Assuming all water reacted with CO, 100% conversion
  If no split then only 58.79% CO needs to get converted

## Slide 19: Material Balances

## Slide 20: Material Balances
Notes: Fixed numbers here

## Slide 21: Energy Balance

## Slide 22: Energy Balance Continued

## Slide 23: Cost of Petroleum Coke
Cost Basis: 2010 Avg. Petroleum Coke through November
4.8 % Sulfur content
$60.95 per ton
$121,900 per day
$4.5 million per year
Electric Power Monthly February 2011

## Slide 24: Short Equipment List
Gasifier | Gasifier (qty 2), Syngas Cooler(qty 2), Synthetic gas Cyclone
ASU (Qty 2) | Oxygen Compressor, Nitrogen Compressor
Syngas Cleanup | Sulfur Plant, Water Gas Shift Reactors
Cooling Water System | Circulating Water Pump, Cooling Tower

## Slide 25: Nitrogen and Oxygen Supply
Currently looking at Linde and Praxair
Deciding on either on-site production or Pipeline
Able to supply O2 and N2 at any required pressure and purity
Looking to be Cost effective

## Slide 26: Report Outline
Final Report:
  Executive Summary
  Discussion
  Recommendations
Appendices
  Design Basis: IP
  Block Flow Diagram: IP
  Process Flow Showing Major Equip.: N/A

## Slide 27: Report Outline
Appendices (Continued)
  Material and Energy Balances: IP
  Calculations: IP
  Annotated Equip. List: N/A
  Econ. Eval. Factored from Equip. Costs: N/A
  Utilities: IP
  Conceptual Control Scheme: N/A
  Major Equipment Layout: N/A

## Slide 28: Report Outline
Appendices (Continued)
  Distribution and End-use Issues: N/A
  Constraints Review: IP
  Applicable Standards: N/A
  Project Communications File: IP
  Information Sources and References: IP

## Slide 29: References
http://www.andrew.cmu.edu/user/kmeister/egroup/bin/Holt_SummaryIGCC_Cost_CCS_03.pdf
Electric Power Monthly February 2011
Higman, Chris, and Maarten Van Der. Burgt. Gasification. Amsterdam: Gulf Professional Pub./Elsevier Science, 2008. Print.
Holt, Neville, Gorge Booras, and Douglas Tadd. A Summary of Recent IGCC Studies of CO2 Capture for Sequestration. Summary. Carnegie Mellon Community, Oct. 2003. Web. 13 Feb. 2011. <http://www.andrew.cmu.edu/user/kmeister/egroup/bin/Holt_SummaryIGCC_Cost_CCS_03.pdf>.
http://www.lenntech.com/periodic/elements/
Moran, Michael J., and Howard N. Shapiro. Fundamentals of Engineering Thermodynamics. Hoboken, N.J. : Chichester: Wiley; John Wiley, 2008. Print.
Maurstad, Ola. An Overview of Coal Based Integrated Gasification Combined Cycle (IGCC) Technology. Rep. Cambridge: Massachusetts Institute of Technology, 2005. For Energy and Environment. Scribd. Web. 2 Feb. 2011. <http://www.scribd.com/doc/35269273/24/Syngas-quenching>.